# Performance Of Equalized I-Q QPSK Over 2-Ray Rayleigh Fading

Adinoyi, A.B. Al-Semari, S.A. Zerguine, A.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Signals, Systems, and Computers, 1999. Conference Record of the Thirty-Third Asilomar conference;Publication Date: 1999;Vol: 1,On page(s): 306-309 vol.1;ISBN: 0-7803-5700-0

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

In many wideband cellular systems, the channel experiences frequency selective fading. This paper evaluates the bit error rate (BER) performance of equalized I-Q QPSK over frequency selective Rayleigh fading channels. I-Q trellis codes were shown to possess excellent inherent minimum time diversity over flat fading Rayleigh channels. However, they have not been examined for frequency-selective fading channels, where channel equalization is required. In this work, I-Q QPSK systems performance over these channels employing a decision feedback equalizer (DFE) is evaluated. Very reliable communication over the mobile channel is obtained using I-Q QPSK combined with interleaving and adaptive equalization compared to the traditional Gray-mapped trellis codes

For pre-prints please write to:abstracts@kfupm.edu.sa