# CMOS Digitally Programmable Inductance

Alzaher, Hussain Tasadduq, Noman;Department of Electrical Engineering, King Fahd University of Petroleum & Minerals, Dhahran, Saudi Arabia, phone: +966-3-8601434; fax: +966-3-8603535; Email: alzaher@kfupm.edu.sa;

Microelectronics, 2006. ICM '06. International conference;Publication Date: 16-19 Dec. 2006; ISBN: 1-4244-0765-6

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A CMOS digitally programmable active lossless inductor realization is proposed. The proposed inductor is based on current and voltage followers and uses R-2R ladder to provide digital tuning of the inductance value. The followers support the use of the simulated inductor for applications in few MHz range. Whereas the use of R-2R provide an additional advantage of realizing high inductance value suitable for very low frequency applications. The proposed inductor is used in synthesizing cascadable biquadratic filters. Simulation results are presented.

For pre-prints please write to:abstracts@kfupm.edu.sa