# Combined Method Based On Inversion And Charge Simulation Forcalculating Electric Stresses In Three-Core Belted Cables

Abdel-Salam, M. Al-Shehri, A.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Generation, Transmission and Distribution [see also IEE Proceedings-Generation, Transmission and Distribution], IEE Proceedings C;Publication Date: Sep 1993;Vol: 140,Issue: 5

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A combined method based on inversion and charge-simulation techniques for calculating the electric field everywhere in three-core belted cables is developed. A small number of simulation charges is required for accurate field determination. The set of equations which describe the potential and field is solved only once with direct determination of the electric potential and field values at any time instant. All of this achieved higher accuracy with a drastic saving in computer time in comparison with previous methods

For pre-prints please write to:abstracts@kfupm.edu.sa