# Radiation From An Open Ended Eccentric Annular Waveguide

Ragheb, H.A.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Antennas and Propagation Society International Symposium, 1997. IEEE., 1997 Digest;Publication Date: 13-18 Jul 1997;Vol: 1,On page(s): 476-479 vol.1;ISBN: 0-7803-4178-3

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

The radiation from an open ended eccentric annular waveguide is examined here. The region between the two circular conductors is assumed to have either symmetrical or anti-symmetrical TE field distribution. The cut-off wavenumber is first calculated and the unknown coefficients in the field are then obtained. It is found that for anti-symmetric field distribution the radiation pattern in the H-plane has a null which can be widely scanned by displacing the conducting core from the central axis. For the symmetrical field distribution a pair of symmetrical nulls in the E-plane are slightly scanned with the displacement of the conducting core. This type of waveguide antenna is useful for applications in phased and adaptive arrays which require null scanning

For pre-prints please write to:abstracts@kfupm.edu.sa