# A Fuzzy Basis Function Network For Generator Excitation Control

Abido, M.A. Abdel-Magid, Y.L.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Fuzzy Systems, 1997., Proceedings of the Sixth IEEE International conference;Publication Date: 1-5 Jul 1997;Vol: 3,On page(s): 1445-1450 vol.3;ISBN: 0-7803-3796-4

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A fuzzy basis function network (FBFN) based power system stabilizer (PSS) is presented in this paper. The proposed FBFN based PSS provides a natural framework for combining numerical and linguistic information in a uniform fashion. The proposed FBFN is trained over a wide range of operating conditions in order to re-tune the PSS parameters in real-time based on generator loading conditions. The orthogonal least squares learning algorithm is developed for designing an adequate and parsimonious FBFN model. Time domain simulations of a synchronous machine equipped with the proposed stabilizer subject to major disturbances are investigated. The performance of the proposed FBFN based PSS is compared with that of a conventional power system stabilizer. The results show the robustness of the proposed FBFN PSS and its ability to enhance system damping over a wide range of operating conditions and system parameter variations

For pre-prints please write to:abstracts@kfupm.edu.sa