# Modified Two-Level State Estimation Approach [For Power Systems]

Habiballah, I.O.;King Fahd Univ. of Pet.Miner., Dhahran;

Generation, Transmission and Distribution, IEE Proceedings-;Publication Date: Mar 1996;Vol: 143,Issue: 2

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

The paper presents modifications to the existing standard decentralised two-level state-estimation approach which imposes conditions on tie power-flow line and boundary-bus power measurements. These conditions are by introducing a modified two-level state-estimation approach which implements modifications to the existing standard approach. The modified approach has no additional requirements at all, except for the observability of the overall system which is an important constraint for any state estimator. A decomposition C-code routine is developed to evaluate the performance of the new concepts associated with the proposed approach. A simple DC power system state estimation network is applied to demonstrate different concepts associated with the proposed approach

For pre-prints please write to:abstracts@kfupm.edu.sa