# Adaptive Seismic Compression By Wavelet Shrinkage

Khene, M.F. Abdul-Jauwad, S.H.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Statistical Signal and Array Processing, 2000. Proceedings of the Tenth IEEE Workshop on;Publication Date: 2000;ISBN: 0-7803-5988-7

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

In this paper, a sophisticated adaptive seismic compression method is presented based on wavelet shrinkage. Our approach combines a time-scale transform with an adaptive non-linear statistical method. First, a discrete 2-D biorthogonal discrete wavelet transform (DWT) is applied to the multi-channel seismic signals to generate a sparse multiresolution (subband) decomposition. Compression is then achieved by shrinking the detail wavelet coefficients using a scale-dependent non-linear soft-thresholding rule. The adaptive scale-dependent thresholds are determined by minimizing the Stein's unbiased risk estimate (SURE). The proposed compression procedure is tested on marine seismic data from the Midyan basin (Red Sea, Saudi Arabia)

For pre-prints please write to:abstracts@kfupm.edu.sa