# Design Of A TE-Pass Reflection Mode Optical Polarizer

Khan, M.A. Jamid, H.A.; Dept. of Electr. Eng., King Fahd Univ. of Pet. & Miner., Dhahran, Saudi Arabia;

Electronics, Circuits and Systems, 2003. ICECS 2003. Proceedings of the 2003 10th IEEE International conference;Publication Date: 14-17 Dec. 2003;Vol: 2,On page(s): 695- 698 Vol.2;ISBN: 0-7803-8163-7

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

In this work, a reflection-mode TE pass polarization filter is proposed and analyzed. Guided TE-polarized waves are highly reflected at the input end of this polarizer. On the other hand guided TM-polarized waves experience very low reflection at the same input end. The TE pass polarizer is realized by adding a corrugation in cascade with a simple three layer metal-clad optical waveguide. The metal-clad section of the polarizer provides the necessary TE/TM discrimination. The corrugated section provides two functions, namely, the necessary high reflectivity and in addition wavelength selectivity. This in addition to being a TE pass reflection mode filter, the device also functions as a narrow band wavelength filter. The analysis of the filter is carried out numerically using the method of lines with a perfectly matched layer in order to absorb the radiative field. A doubling and cascading algorithm is also utilized to efficiently account for the large number of grating periods forming the corrugated section of the filter.

For pre-prints please write to:abstracts@kfupm.edu.sa