# Ultrasonic Wave Transmission In Periodically Undulated Plates

Hawwa, M.A.; Dept. of Mech. Eng., King Fahd Univ. of Pet. & Miner., Dhahran, Saudi Arabia;

Ultrasonics, Ferroelectrics and Frequency Control, IEEE Transactions on;Publication Date: Oct. 2005;Vol: 52,Issue: 10

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

This study focuses on quantifying the change in phase speed of waves transmitting through periodically undulated plates under pass band interaction. A perturbation technique is used to analyze the transmission of horizontally polarized guided waves in elastic plates with sinusoidal periodicity at their outerfaces. Phase speed of transmitting modes is presented as a function of various parameters, including outerface wavenumber, undulation amplitude, degree of undulations symmetry about the periodically undulated plate midplane, plate average thickness, arid frequency of propagation.

For pre-prints please write to:abstracts@kfupm.edu.sa