# Adaptive Predictive Power Control For The Uplink Channel In DS-CDMA Cellular Systems

Aldajani, M.A. Sayed, A.H.; King Fahd Univ. of Pet. & Miner.s, Dhahran, Saudi Arabia;

Vehicular Technology, IEEE Transactions on;Publication Date: Nov. 2003;Vol: 52,Issue: 6

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

In this paper, we analyze the conventional closed-loop power-control system. We explain that the system behaves essentially as a companded delta modulator and then derive an expression for the power-control error in terms of the channel fading, which suggests methods for reducing the error variance. This is achieved by using a prediction technique for estimating the channel-power fading profile. The prediction module is combined with several proposed schemes for closed-loop power control. The resulting architectures are shown to result in improved performance in simulations.

For pre-prints please write to:abstracts@kfupm.edu.sa