# Spacecraft Spin Axis Attitude Determination

Emara-Shabaik, H.E.;Dept. of Syst. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Aerospace and Electronic Systems, IEEE Transactions on;Publication Date: Apr 1992;Vol: 28,Issue: 2

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A mathematical formulation of the spacecraft spin axis attitude determination problem in the form of a norm constrained-least-squares minimization problem is provided. The formulation has a mathematically transparent interpretation as a search for the optimal unit vector on the surface of the unit sphere. Two algorithms are developed and compared by simulation. The results show a tradeoff between estimation accuracy and computational requirements. One algorithm is about three times more accurate than the other and is therefore recommended even though it requires about 20% more in computer storage and operations, and about 50% more in central processing unit time

For pre-prints please write to:abstracts@kfupm.edu.sa