# Effect Of Bit-Threshold Errors On The Harmonic And Intermodulationperformance Of Successive Approximation A/D Converters

Abuelma'atti, M.T.;King Fahd Univ. of Pet.Miner., Dhahran;

Communications, IEEE Transactions on;Publication Date: Aug 1993;Vol: 41,Issue: 8

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A simple approach is described for predicting the harmonic and intermodulation performance of a real successive approximation analog-to-digital converter (ADC) with bit-threshold errors. The real ADC characteristic is split into an ideal staircase characteristic, representing the ideal ADC characteristic, minus a train of pulses, representing the bit-threshold errors. Series expressions are obtained for the output spectra of the real ADC excited by a multicarrier input signal with arbitrary amplitudes. The special case of two equal-amplitude carriers is considered in detail, and analytical expressions are obtained for the amplitudes of the harmonic and intermodulation products in terms of the individual bit-threshold errors. The feasibility of minimizing the amplitudes of the intermodulation products is explored

For pre-prints please write to:abstracts@kfupm.edu.sa