# Spatial Domain Modeling Of Microcellular Systems Operating In Multipath Nakagami Channels

Muhammed, S. Al-Ahmadi Shiekh, A.U.H.; Dept. of Electr. Eng., King Fahd Univ. of Pet. & Miner., Dhahran, Saudi Arabia;

Personal, Indoor and Mobile Radio Communications, 2002. The 13th IEEE International Symposium on;Publication Date: 15-18 Sept. 2002;Vol: 4,On page(s): 1942- 1946 vol.4;ISBN: 0-7803-7589-0

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

In conventional channel models, the AoA's at the BS, are assumed to be uniformly distributed. However, measurements in urban areas have shown non-uniform AoA distributions. In this paper, the spatial characterization of wideband urban mobile radio channels is investigated and the resulting and spatial correlations at the BS receiver are computed. A geometrically based modeling is used to spatially characterize both TU and BU environments. The clustered scatterers are assumed to have bivariate Gaussian densities. The AoA pdf's are derived. The spatial correlations are computed for tooth environments and the effects of the channel parameters such as the scatterer's variance, the BS-MS distance, the mean angle of arrival on these correlations are investigated.

For pre-prints please write to:abstracts@kfupm.edu.sa