# Analysis Of The Effect Of Radio Frequency Interference On The DC Performance Of CMOS Operational Amplifiers

Taher Abuelmaatti, M.; King Fahd Univ. of Pet. & Minerals, Dhahran, Saudi Arabia;

Electromagnetic Compatibility, 2003. EMC '03. 2003 IEEE International Symposium on;Publication Date: 11-16 May 2003;Vol: 1,On page(s): 355- 358 Vol.1;  ISBN: 0-7803-7779-6

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

Fourier-series approximations are obtained for the input-output characteristic of the CMOS asymmetrical differential amplifier. Using these approximations, the DC voltage offset of a CMOS differential amplifier subjected to RF interference can be studied and analytical expressions are obtained. These expressions can help in optimizing the parameters of the CMOS differential amplifier to minimize the offset voltage resulting from the RF interference.

For pre-prints please write to:abstracts@kfupm.edu.sa