# Adaptive Control Of Nonlinear Hammerstein Model Using NLMS Filter

Shafiq, M. Al-Sunni, F.M. Farooq, S.O.; Dept. of Syst. Eng., King Fahd Univ. of Pet. & Miner., Dhahran, Saudi Arabia;

Electronics, Circuits and Systems, 2003. ICECS 2003. Proceedings of the 2003 10th IEEE International conference;Publication Date: 14-17 Dec. 2003;Vol: 2,On page(s): 439- 442 Vol.2;ISBN: 0-7803-8163-7

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A novel technique, using the normalized least mean squares (NLMS) adaptive filter is proposed for adaptive control of the plant dynamics of a nonlinear plant. The nonlinear plant considered belongs to the Hammerstein type of nonlinear system. Stable adaptive controller for a stable discrete time nonlinear plant is designed. The nonlinear plant considered may be non-minimum phase. The controller is composed of an adaptive finite impulse response (FIR) filter in the feedback loop. This adaptive FIR filter is designed online as an L-delay approximate inverse system of the given stable nonlinear plant.

For pre-prints please write to:abstracts@kfupm.edu.sa