# Simultaneous Design Of Damping Controllers And Internal Controllers Of A Unified Power Flow Controller

Abido, M.A. Al-Awami, A.T. Abdel-Magid, Y.L.; King Fahd Univ. of Pet. & Miner., Dhahran, Saudi Arabia;

Power Engineering Society General Meeting, 2006. IEEE;Publication Date: 18-22 June 2006;  ISBN: 1-4244-0493-2

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

In this paper, the use of a supplementary controller of a unified power flow controller (UPFC) to damp low frequency oscillations is investigated. A new technique to design UPFC damping controllers simultaneously with UPFC internal controllers is proposed. An optimization problem to search for the optimal controller settings is formulated so as to optimize a time-domain based objective function that considers all the controllers simultaneously. The effectiveness of the proposed controllers in damping low frequency oscillations is verified through eigenvalue analysis and non-linear time simulation. A comparison with a sequential design of the controllers under study is also .included.

For pre-prints please write to:abstracts@kfupm.edu.sa