# Coordinated Design Of Robust Excitation And TCSC-Based Damping Controllers

Abido, M.A. Abdel-Magid, Y.L.; Dept. of Electr. Eng., King Fahd Univ. of Pet. & Miner., Dhahran, Saudi Arabia;

Power Engineering Society General Meeting, 2003, IEEE;Publication Date: 13-17 July 2003;Vol: 3,On page(s): - 1731 Vol. 3;ISBN: 0-7803-7989-6

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

Power system stability enhancement via robust coordinated design of a power system stabilizer (PSS) and a thyristor-controlled series capacitor (TCSC)-based stabilizer is thoroughly investigated in this paper. The coordinated design problem of robust excitation and TCSC-based controllers over a wide range of loading conditions and system configuration is formulated as an optimization problem with an eigenvalue-based objective function. The real-coded genetic algorithm (RCGA) is employed to search for optimal controller parameters. This study also presents a singular value decomposition (SVD) based approach to assess and measure the controllability of the poorly damped electromechanical modes by different control inputs. The damping characteristics of the proposed control schemes are also evaluated in terms of the damping torque coefficient over a wide range of loading conditions. The proposed stabilizers were tested on a weakly connected power system. The damping torque coefficient analysis, nonlinear simulation results, and eigenvalue analysis show the effectiveness and robustness of the proposed approach over a wide range of loading conditions.

For pre-prints please write to:abstracts@kfupm.edu.sa