# High Speed Multi-Stage Code Search Algorithm In CELP

Elshafei, M. Al-Suwaiyel, M.I.;King Fahd Univ. of Pet.Miner., Dhahran;

Global Telecommunications Conference, 1991. GLOBECOM '91. 'Countdown to the New Millennium. Featuring a Mini-Theme on: Personal Communications Services;Publication Date: 2-5 Dec 1991;ISBN: 0-87942-697-7

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

An efficient multistage algorithm for code search in the code excited linear prediction (CELP) methods of speech coding is described. The algorithm requires binary clustering of the codebook into a fixed number of cells and inverse filtering of the incoming speech by the format and pitch filters to produce a residual error sequence (RES). It is demonstrated that the method could achieve a reduction in the number of operations from 40 to 50 times. It is shown that codebooks constructed from random walk stochastic sequences improve the average signal to noise ratio by 5-6 dB over codebooks constructed from Gaussian white noise sequences

For pre-prints please write to:abstracts@kfupm.edu.sa