# U-Model Based Adaptive Tracking Scheme For Unknown MIMO Bilinear Systems

Azhar, A.S.S. Al-Sunni, F.M. Shafiq, M.;Dept. of Electr. Eng., King Fahd Univ. of Pet. & Miner., Dhahran;

Industrial Electronics and Applications, 2006 1ST IEEE conference;Publication Date: 24-26 May 2006;ISBN: 0-7803-9514-X

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

Bilinear systems are attractive candidates for many dynamical processes, since they allow a significantly larger class of behaviour than linear systems, yet retain a rich theory which is closely related to the familiar theory of linear systems. A new technique for the control of unknown MIMO bilinear systems is introduced. The scheme is based on the U-model with identification based on radial basis functions neural networks which is known for mapping any nonlinear function. U-model is a control oriented model used to represent a wide range of non-linear discrete time dynamic plants. The proposed tracking scheme is presented and verified using simulation examples

For pre-prints please write to:abstracts@kfupm.edu.sa