# Fast Methods For Code Search In CELP

Ahmed, M.E. Al-Suwaiyel, M.I.;King Fahd Univ. of Pet.Miner., Dhahran;

Speech and Audio Processing, IEEE Transactions on;Publication Date: Jul 1993;Vol: 1,Issue: 3

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

The code excited linear prediction (CELP) technique has the potential for producing high quality synthetic speech at bit rates as low as 4.8 kb/s. Three fast search methods for selecting an optimal excitation sequence from a code book of stochastic vectors are described. The key idea is to inverse-filter the actual speech with the formant and pitch filters to produce a residual error sequence (RES). The residual error is used to identify a neighborhood or a subset of codes for further processing. The first method, called dynamic nearest neighborhood (DNN), attempts to dynamically construct a neighborhood of the K codes of maximum correlation with the residual error. The second method, called nearest fixed neighborhood (NFN), clusters the code book into a fixed number of cells, and code search is performed on the codes of the cell nearest to the RES. The two methods achieve a reduction in the search procedure by a factor of 8-20 times. The third method combines the advantages of the first two methods to attain a reduction from 40 to 50 times. The performance of these techniques and some of their ramifications are addressed

For pre-prints please write to:abstracts@kfupm.edu.sa