# A General Expression For The Capacity Of Slotted ALOHA UnderNakagami Fading

Al-Semari, S.A. Grami, N.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Wireless Communications and Networking Conference, 1999. WCNC. 1999 IEEE;Publication Date: 1999;ISBN: 0-7803-5668-3

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A general expression for the channel throughput of slotted ALOHA under Nakagami fading is obtained assuming different fading statistics and unequal average power levels for the desired and the interfering packets. The expression provides a better alternative to the previously reported expressions derived under similar conditions. With this general expression the effect of the use of modulation on the system performance is then studied. It is observed that the inclusion of the deleterious effects like white noise, bit error rate and the packet length reduces the throughput over the one observed under idealized conditions

For pre-prints please write to:abstracts@kfupm.edu.sa