# Electromagnetic Scattering From A Coaxial Dielectric Circularcylinder Loading A Semicircular Gap In A Ground Plane

Ragheb, H.A.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Microwave Theory and Techniques, IEEE Transactions on;Publication Date: Jun 1995;Vol: 43,Issue: 6

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

An exact dual series solution of a plane wave incident on a coaxial dielectric circular cylinder imbedded in a semicircular gap of a ground plane is presented. Both TM and TE cases are considered here. The scattered field is represented in terms of an infinite series of cylindrical waves with unknown coefficients. By applying the boundary conditions and employing the partial orthogonality of the trigonometric functions the scattering coefficients are obtained. The resulting infinite series is then truncated to a finite number of terms to produce numerical results. For the sake of comparison with the published data some special cases are introduced first. The comparisons showed excellent agreement in all cases

For pre-prints please write to:abstracts@kfupm.edu.sa