# Modeling Of Magnetization Curves For Computer-Aided Design

Abuelman'atti, M.T.;King Fahd Univ. of Pet.Miner., Dhahran;

Magnetics, IEEE Transactions on;Publication Date: Mar 1993;Vol: 29,Issue: 2

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A simple algorithm is presented for obtaining the coefficients of the sine-series function for modelling the magnetization curves of magnetic materials. The algorithm, which can represent the fine details of the magnetization curve, can be easily implemented in mainframe computers and scientific programmable calculators, and can yield the coefficients of sine-series functions with any number of terms. Using the proposed algorithm, sine-series functions can be obtained for nearly rectangular magnetization curves with any required accuracy both in the high-flux and in the low-flux regions. The algorithm can be used for obtaining the Fourier components of an unfolded hysteresis loop

For pre-prints please write to:abstracts@kfupm.edu.sa