# A New Current-Controlled Multiple-Output Current-Conveyor

Abuelma'atti, M.T. Abed, S.M.;King Fahd Univ. of Pet.Miner., Dhahran;

Circuits and Systems, 1997. ISCAS '97., Proceedings of 1997 IEEE International Symposium on;Publication Date: 9-12 Jun 1997;Vol: 2,On page(s): 961-964 vol.2;ISBN: 0-7803-3583-X

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A new second-generation multiple-output current-controlled current-conveyor (MOCCCC) is presented. It has current-transfer ratios that can be varied by control currents. It is characterized by approximately constant bandwidth over a wide range of current-transfer ratios. The MOCCCC is then used as a building block for realizing electronically-tunable second-order bandpass/lowpass filters. Spice simulation results are presented

For pre-prints please write to:abstracts@kfupm.edu.sa