# Downlink Channel Estimation For IMT-DS

Faisal, S. Shah, A. Sheikh, A.U.H.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Personal, Indoor and Mobile Radio Communications, 2001 12th IEEE International Symposium on;Publication Date: Sep/Oct 2001;Vol: 2,On page(s): E-137-E-141 vol.2;ISBN: 0-7803-7244-1

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

IMT-DS system is an approved terrestrial radio interface standard for 3G mobile communication based on direct sequence code division multiple access (DS-CDMA). It employs a RAKE receiver to exploit multipath diversity. This paper discusses a new dimension in DS-CDMA channel estimation i.e., chip-level adaptive channel estimation. The DL channel of an IMT-DS system consists of time-multiplexed pilot and data symbols to facilitate coherent detection. To obtain channel estimates during pilot symbols, we propose a chip level adaptive channel estimation which performs better than the conventional method. For slow fading channels, like a pedestrian channel, zero order interpolation provides satisfactory performance. However, for fast fading channels, a common decision directed algorithm is applied whose performance is limited due to error propagation. The proposed schemes are assessed over the IMT-DS system by performing simulations

For pre-prints please write to:abstracts@kfupm.edu.sa