# Simultaneous Stabilisation Of Power Systems Using Geneticalgorithms

Abdel-Magid, Y.L. Bettayeb, M. Dawoud, M.M.;Dept. of Electr. Eng., King Fahd Univ. of Pet.Miner., Dhahran;

Generation, Transmission and Distribution, IEE Proceedings-;Publication Date: Jan 1997;Vol: 144,Issue: 1

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

The paper considers the simultaneous stabilisation of a power system over a wide range of operating conditions via a single power system stabiliser using genetic algorithms. A power system operating at various load levels is treated as a finite set of plants. The problem of selecting the parameters of a power system stabiliser which simultaneously stabilises this set of plants is converted to a simple optimisation problem which is solved by a genetic algorithm and an eigenvalue-based objective function. A single-machine infinite bus system is considered to demonstrate the suggested technique

For pre-prints please write to:abstracts@kfupm.edu.sa