A Tabu Search Algorithm For Maintenance Scheduling Of Generating Units

El-Amin, I; Duffuaa, S; Abbas, M

ELSEVIER SCIENCE SA, ELECTRIC POWER SYSTEMS RESEARCH; pp: 91-99; Vol: 54

King Fahd University of Petroleum & Minerals

http://www.kfupm.edu.sa

Summary

A new heuristic algorithm based on the Tabu search has been proposed for the maintenance schedule (MS) of electric generation units. The algorithm was developed, implemented and tested on an integrated model for the MS problem. The model. used two criteria: minimizing the total generator operating cost and levering the reserve. Each of the above criteria is used with the following constraints: maintenance completion, crew size, precedence, reserve and reserve constants. The performance of the Tabu search algorithm is promising. The Tabu search algorithm solved two power system problems, 4 units and 22 units. The implicit enumeration algorithm was used to check the validity and the quality of the Tabu search solution. (C) 2000 Published by Elsevier Science S.A. All rights reserved.

References:

- ALKHAMIS TM, 1992, IEEE T POWER SYST, V7, P933

- BENDAYA M, 1997, J PROD PLANNING CONT, V18, P694

- DOPAZO JF, 1975, IEEE T POWER APPARAT, V94, P1537

- ESCUDERO LF, 1980, IEEE CAT 80 CH IEEE

- GLOVER F, 1986, COMPUT OPER RES, V13, P563

- GLOVER F, 1989, ORSA J COMPUTING, V1, P190

- GLOVER F, 1990, MANAGE DECIS ECON, V11, P365

- GLOVER F, 1990, ORSA J COMPUTING, V2, P4

- GLOVER F, 1990, TABU SEARCH TUTORIAL

- HANSEN P, 1987, 4387 RR RUTCOR

- KNOX J, 1989, THESIS U COLORADO BO

- KRALJ B, 1994, INT J ELECT POWER EN, V16, P24

- SATOH T, 1991, IEEE T POWER SYST, V6, P850

- SKORINKAPOV J, 1990, ORSA J COMPUTING, V2, P33

- YAMAYEE ZA, 1982, IEEE T POWER APPARAT, V101, P2770

- YELLEN J, 1992, IEEE T POWER SYST, V7, P726

For pre-prints please write to: abstracts@kfupm.edu.sa